## Slide 1: CSC 2224: Parallel Computer Architecture and Programming DRAM. Part 2
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the slides of
Vivek Seshadri, Donghyuk Lee, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU

## Slide 2: Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture
Donghyuk Lee, Yoongu Kim, Vivek Seshadri, Jamie Liu, Lavanya Subramanian, Onur Mutlu
Published in the proceedings of 19th IEEE International Symposium on
High Performance Computer Architecture 2013

## Slide 3
DRAM Stores Data as Charge
1. Sensing
2. Restore
3. Precharge
DRAM cell
Sense amplifier
Three steps of charge movement
Notes: The right figure shows DRAM organization which is consists of DRAM cells and sense-amplifiers.
There are three steps for accessing DRAM.
First, when DRAM selects one of rows in its cell array, the selected cells drive their charge to sense-amplifiers.
Then, sense-amplifiers detect the charge, recognizing data of cells.
We call this operation as sensing.
Second, after sensing data from DRAM cells, sense-amplifiers drive charge to the cells for reconstructing original data.
We call this operation as restore.
Third, after restoring the cell data, DRAM deselects the accessed row and puts the sense-amplifiers to original state for next access.
We call this operation as precharge.
As shown in these three steps, DRAM operation is charge movement between cell and sense-amplifier.

## Slide 4
Sensing
Restore
Timing Parameters
Data 0
Data 1
cell
time
charge
Sense amplifier
DRAM Charge over Time
Why does DRAM need the extra timing margin?
In theory
margin
cell
Sense amplifier
In practice
Notes: Timing parameters exist to ensure sufficient movement of charge.
The figure shows the timeline for accessing DRAM in X-axis and Y-axis shows the charge amount in DRAM cell and sense-amplifier.
When selecting a row of cells, each cell drives their charge toward to the corresponding sense-amplifier.
If driven charge is more than enough to detect the data, the sense-amplifier starts to restore data by driving charge toward the cell.
This restore operation finishes when the cell is fully charged.
Ideally, DRAM timing parameters are just enough for the sufficient movement of charge.
However, in practice, there are large margin in DRAM timing parameters.
Why are these margin required?

## Slide 5
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cell that can store small amount of charge
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Two Reasons for Timing Margin
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cell that can store small amount of charge;
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cells that can store large amount of charge
Notes: There are two reasons for the margin in DRAM timing parameters.
First is process variation and second is temperature dependence.
Let me introduce the first factor, process variation.

## Slide 6
Same size 
Same charge 
Different size 
Different charge 
Same latency
Different latency
Large variation in cell size 
Large variation in charge 
Large variation in access latency
DRAM Cells are Not Equal
Real
Ideal
Largest cell
Smallest cell
Notes: Ideally, DRAM would have uniform cells which have same size, thereby having same access latency.
Unfortunately, due to process variation, each cell has different size, thereby having different access latency.
Therefore, DRAM shows large variation in both charge amount in its cell and access latency to its cell.

## Slide 7
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cells that can store large amount of charge
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Two Reasons for Timing Margin
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Notes: There are two reasons for the margin in DRAM timing parameters.
First is process variation and second is temperature dependence.
Let me introduce the first factor, process variation.

## Slide 8
Cells store small charge at high temperature
and large charge at low temperature
 Large variation in access latency
Charge Leakage Temperature
Room Temp.
Hot Temp. (85°C)
Small leakage
Large leakage
Notes: DRAM leakage increases the variation.
DRAM loses their charge over time and loses more charge at higher temperature.
Therefore, DRAM cell has smallest charge when operating at hot temperature, for example 85C which is the highest temperature guaranteed by DRAM standard.
This temperature dependence increases the variation in DRAM cell charge.

## Slide 9
DRAM Timing Parameters
DRAM timing parameters are dictated by the worst case
  The smallest cell with the smallest charge in all DRAM products
  Operating at the highest temperature
Large timing margin for the common case
Can lower latency for the common case

## Slide 10: DRAM Testing Infrastructure
Temperature
Controller
PC
Heater
FPGAs
FPGAs
Notes: This is the photo of our infrastructure, that we built mostly from scratch.
For higher throughput, we employ eight FPGAs, all of which are enclosed in thermally-regulated environment.

## Slide 11
Typical DIMM at
Low Temperature
Obs 1. Faster Sensing
More charge
Strong charge
flow
Faster sensing
Typical DIMM at Low Temperature
 More charge  Faster sensing
Timing
(tRCD)
17% ↓
No Errors
115 DIMM
characterization
Notes: First step in DRAM operation is sensing.
In typical case, there are more charge in DRAM cell compared to the worst case.
The excessive charge enables stronger charge drive to sense-amplifier.
Then, sense-amplifier can detect data of DRAM cell fast, thereby complete sensing operation fast.
In our DRAM latency profiling results of 115 DRAM modules,
we observe that 17% potential reduction for the corresponding timing parameters of sensing.
As a result, more charge in typical cases lead to fast sensing.

## Slide 12
Obs 2. Reducing Restore Time
Larger cell &
Less leakage 
Extra charge
No need to fully
restore charge
Typical DIMM at lower temperature
 More charge  Restore time reduction
Read (tRAS)
37% ↓
Write (tWR)
54% ↓
No Errors
115 DIMM
characterization
Typical DIMM at
Low Temperature
Notes: Second step in DRAM operation is restore.
Due to larger size and less leakage, typical DRAM cells have more charge than the worst cell.
Even though typical DRAM does not restore the excessive charge during restore operation,
eventually the typical cell has more charge than the worst case cell, guaranteeing reliable operations.
By reducing this restore time in DRAM read/write, our DRAM latency characterization shows significant potential to reduce corresponding timing parameters. For example, 37% for read and 54% for write.
As a result, more charge in typical cases enables restore time reduction.

## Slide 13
Empty (0V)
Full (Vdd)
Half
Obs 3. Reducing Precharge Time
Bitline
Sense amplifier
Sensing
Precharge
Precharge ?
– Setting bitline to half-full charge
Typical DIMM at
Low Temperature
Notes: Third step is precharge. Previously we explained the precharge simply as going back to original state.
Let me introduce more details about precharge.
To detect data in DRAM cell, DRAM has sense-amplifier and wire connection to the bitline.
DRAM preserve their a bit of data in two charge state, empty and fully charged.
During sensing and restore, the bitline moves to either of these two states.
After finishing the access, the bitline should be go back to the half of these two state.
We call this precharge. Unfortunately, bitline is usually long by connecting hundred of cells such that it takes long time for precharge.

## Slide 14
Empty (0V)
Full (Vdd)
Half
bitline
Not fully precharged
More charge
 strong sensing
Access empty cell
Access full cell
Timing
(tRP)
35% ↓
No Errors
115 DIMM
characterization
Typical DIMM at Lower Temperature
 More charge  Precharge time reduction
Obs 3. Reducing Precharge Time
Notes: Let us observe the impact of reducing precharge with a simple example.
The sense-amplifier first accesses an empty cell then not fully precharged by reducing corresponding timing parameter.
Then DRAM next access a fully charged cell.
Due to the bias in the bitline, it takes longer time to access the fully charged cell.
However, if the cell has much excessive charge, the strong charge flow overcomes the bias in the bitline, leading to reliable access.
Our DRAM latency evaluation shows that in typical case, we can reduce corresponding timing parameter by 35% without errors.
Therefore, more charge in typical cases enables precharge time reduction.

## Slide 15: Adaptive-Latency DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer profiles multiple sets of
  reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature

## Slide 16
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi-Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
Real System Evaluation
AL-DRAM provides high performance improvement, greater for multi-core workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 17
Summary: AL-DRAM
Observation
  DRAM timing parameters are dictated by the worst-case cell (smallest cell at highest temperature)
Our Approach: Adaptive-Latency DRAM (AL-DRAM)
  Optimizes DRAM timing parameters for the common case (typical DIMM operating at low temperatures)
Analysis: Characterization of 115 DIMMs
  Great potential to lower DRAM timing parameters (17 – 54%) without any errors
Real System Performance Evaluation
  Significant performance improvement (14% for memory-intensive workloads) without errors (33 days)
Notes: Let me summarize.
DRAM timing parameters are dictated by the worst case cell.
We propose Adaptive-Latency DRAM that optimizes DRAM timing parameters for common cases
Our characterization shows the significant potential to lower DRAM timing parameters.
Our real system evaluation shows that our mechanism provides significant performance improvement without introducing errors.

## Slide 18: Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case
Donghyuk Lee, Yoongu Kim,
Gennady Pekhimenko, Samira Khan, Vivek Seshadri, Kevin Chang, and Onur Mutlu
Published in the proceedings of 21st
International Symposium on High Performance Computer Architecture 2015

## Slide 19: Outline
What is DRAM?
DRAM Internal Organization
Problems and Solutions
  Latency (Tiered-Latency DRAM, HPCA 2013;
  Adaptive-Latency DRAM, HPCA 2015)
  Parallelism (Subarray-level Parallelism, ISCA 2012)

## Slide 20: Parallelism: Demand vs. Supply
Demand
Supply
Out-of-order Execution
Multi-cores
Prefetchers
Multiple
Banks

## Slide 21: Increasing Number of Banks?
How to improve available parallelism within DRAM?
Adding more banks → Replication of shared structures
Replication → Cost

## Slide 22: Our Observation
Time
1. Wordline enable
2. Charge sharing
3. Sense amplify
4. Charge restoration
5. Wordline disable
6. Restore sense-amps
Data Access
Local to a subarray

## Slide 23: Subarray-Level Parallelism
Row Decoder
1
0
0
1
1
0
0
1
Row Decoder
Row Address
Column Read/Write
Row Address
Row Address
Replicate
Time share

## Slide 24: Subarray-Level Parallelism: Benefits
Time
Data Access
Data Access
Data Access
Data Access
Saved Time
Commodity DRAM
Subarray-Level Parallelism
Two requests to different subarrays in same bank

## Slide 25: Results Summary
Chart: 
| Performance
Commodity DRAM | 1
SALP | 1.17
Chart: 
| Energy Consumption
Commodity DRAM | 1
SALP | 0.81
Commodity DRAM
Subarray-Level Parallelism
17%
19%

## Slide 26: A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM
Yoongu Kim, Vivek Seshadri, Donghyuk Lee, Jamie Liu, Onur Mutlu
Published in the proceedings of 39th
International Symposium on Computer Architecture 2012

## Slide 27: CSC 2224: Parallel Computer Architecture and Programming Advanced Memory
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the slides of
Vivek Seshadri, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU

## Slide 28: Review #5
Flipping Bits in Memory Without Accessing Them Yoongu Kim et al., ISCA 2014

## Slide 29: Review: Memory Latency Lags Behind
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 30: We Need A Paradigm Shift To …
Enable computation with minimal data movement
Compute where it makes sense (where data resides)
Make computing architectures more data-centric

## Slide 31: Processing Inside Memory
Many questions … How do we design the:
  compute-capable memory & controllers?
  processor chip?
  software and hardware interfaces?
  system software and languages?
  algorithms?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 32: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures
Pull from Systems and Applications
  Data access is a major system and application bottleneck
  Systems are energy limited
  Data movement much more energy-hungry than computation
Dally, HiPEAC 2015

## Slide 33: Two Approaches to In-Memory Processing
1. Minimally change DRAM to enable simple yet powerful computation primitives
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses (Seshadri et al., MICRO 2015)
2. Exploit the control logic in 3D-stacked memory to enable more comprehensive computation near memory
  PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture (Ahn et al., ISCA 2015)
  A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing (Ahn et al., ISCA 2015)
  Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation (Hsieh et al., ICCD 2016)

## Slide 34: Approach 1: Minimally Changing DRAM
DRAM has great capability to perform bulk data movement and computation internally with small changes
  Can exploit internal bandwidth to move data
  Can exploit analog computation capability
  …
Examples: RowClone, In-DRAM AND/OR, Gather/Scatter DRAM
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses (Seshadri et al., MICRO 2015)

## Slide 35: Starting Simple: Data Copy and Initialization
Bulk Data Copy
Bulk Data Initialization
src
dst
dst
val

## Slide 36: Bulk Data Copy and Initialization
Bulk Data Copy
Bulk Data Initialization
src
dst
dst
val

## Slide 37: Bulk Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 38: Today’s Systems: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 39: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 40: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
Notes: copy

## Slide 41: RowClone: Intra-Subarray
VDD/2
VDD/2
0
VDD/2 + δ
0
VDD
VDD
VDD/2 + δ
Sense Amplifier
(Row Buffer)
Amplify the difference
0
Data gets copied
src
dst

## Slide 42: RowClone: Intra-Subarray (II)
r
c
r
o
w
s
s
t
o
w
d
r
Row Buffer
r
c
r
o
w
s
s
r
c
r
o
w
1. Activate src row (copy data from src to row buffer)
2. Activate dst row (disconnect src from row buffer, connect dst – copy data from row buffer to dst)

## Slide 43: RowClone: Inter-Bank
Memory Channel
Chip I/O
Bank
Shared internal bus
Overlap the latency of the read and the write
1.9X latency reduction, 3.2X energy reduction

## Slide 44: Generalized RowClone
Memory Channel
Chip I/O
Bank
Bank I/O
Subarray
Intra Subarray
Copy (2 ACTs)
Inter Bank Copy
(Pipelined
Internal RD/WR)
Inter Subarray Copy
(Use Inter-Bank Copy Twice)
0.01% area cost

## Slide 45: RowClone: Fast Row Initialization
0
0
0
0
0
0
0
0
0
0
0
0
Fix a row at Zero
(0.5% loss in capacity)

## Slide 46: RowClone: Bulk Initialization
Initialization with arbitrary data
  Initialize one row
  Copy the data to other rows
Zero initialization (most common)
  Reserve a row in each subarray (always zero)
  Copy data from reserved row (FPM mode)
  6.0X lower latency, 41.5X lower DRAM energy
  0.2% loss in capacity

## Slide 47: RowClone: Latency & Energy Benefits
Chart: Latency Reduction
| Intra-Subarray | Inter-Bank | Inter-Subarray | Intra-Subarray | Copy | Zero
Latency | 11.62 | 1.93 | 0.99 | 6.06
Chart: Energy Reduction
| Intra-Subarray | Inter-Bank | Inter-Subarray | Intra-Subarray | Copy | Zero
Energy | 74.4 | 3.2 | 1.5 | 41.5
11.6x
1.9x
6.0x
1.0x
74.4x
3.2x
1.5x
41.5x
Very low cost: 0.01% increase in die area

## Slide 48: Copy and Initialization in Workloads
Chart: Fraction of Memory Traffic
| bootup | compile | forkbench | mcached | mysql | shell
Read | 0.27394 | 0.34894 | 0.054305 | 0.45435 | 0.43893 | 0.099545
Write | 0.27185 | 0.33217 | 0.32279 | 0.45421 | 0.43769 | 0.089756
Copy | 0.21551 | 0 | 0.61578 | 0 | 0 | 0.42016
Zero | 0.23871 | 0.31889 | 0.007122 | 0.091442 | 0.12338 | 0.39054

## Slide 49: RowClone: Application Performance
Chart: % Compared to Baseline
| bootup | compile | forkbench | mcached | mysql | shell
IPC Improvement | 15 | 9 | 43 | 4 | 4 | 40
Energy Reduction | 40 | 32 | 60 | 15 | 17 | 67

## Slide 50: End-to-End System Design
DRAM (RowClone)
Microarchitecture
ISA
Operating System
Application
How to communicate occurrences of bulk copy/initialization across layers?
How to maximize latency and energy savings?
How to ensure cache coherence?
How to handle data reuse?

## Slide 51: Ambit In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology
Vivek Seshadri
Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand, Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, Todd C. Mowry

## Slide 52: Executive Summary
Problem: Bulk bitwise operations
  present in many applications, e.g., databases, search filters
  existing systems are memory bandwidth limited
Our Proposal: Ambit
  perform bulk bitwise operations completely inside DRAM
  bulk bitwise AND/OR: simultaneous activation of three rows
  bulk bitwise NOT: inverters already in sense amplifiers
  less than 1% area overhead over existing DRAM chips
Results compared to state-of-the-art baseline
  average across seven bulk bitwise operations
    32X performance improvement, 35X energy reduction
  3X-7X performance for real-world data-intensive applications
Notes: Talk about energy more
Explicitly state the performance improvement numbers
Range for throughput and energy?
Color more? Bulk AND/OR or NOT
Mechanism for NOT – fix the description. (use inverters already in sense amplifiers}?
Cost not coming out – mention the area cost

## Slide 53
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017
Bulk Bitwise Operations
BitWeaving
(database queries)
BitFunnel
(web search)
Bitmap indices
(database indexing)
Set operations
Encryption algorithms
DNA
sequence mapping
...
Notes: Add … (signify more applications)
Add references to some works (bitweaving, bitfunnel)

## Slide 54: Today, DRAM is just a storage device!
Processor
(CPU, GPU, FPGA)
DRAM
Channel
Write
Read
Throughput of bulk bitwise operations limited by available memory bandwidth

## Slide 55: Our Approach
Processor
(CPU, GPU, FPGA or PiM)
DRAM
Channel
Use analog operation of DRAM to perform bitwise operations completely inside memory!

## Slide 56: Inside a DRAM Chip
…
…
…
…
…
…
2D Array
of DRAM Cells
Sense amplifiers
8KB

## Slide 57: DRAM Cell Operation
Sense Amp
enable
bitline
wordline
capacitor
access transistor
bitline

## Slide 58: DRAM Cell Operation
½ VDD + δ
enable
bitline
wordline
capacitor
access transistor
0
½ VDD
0
1
1
VDD
raise wordline
enable sense amp
connects cell to bitline
cell loses charge to bitline
cell regains charge
Sense Amp
deviation in bitline voltage
½ VDD
0
bitline

## Slide 59: Triple-Row Activation: Majority Function
½ VDD + δ
0
½ VDD
0
1
1
VDD
enable sense amp
Sense Amp
activate
all three rows
0
1
0
1

## Slide 60: Bitwise AND/OR Using Triple-Row Activation
1
1
1
1
VDD
Sense Amp
A
B
C

## Slide 61: Bitwise AND/OR Using Triple-Row Activation
1
1
1
1
VDD
Sense Amp
A
B
C
Output = AB + BC + CA
= C (A OR B) +
~C (A AND B)
Control the value of C to perform bitwise OR or bitwise AND of A and B
38X improvement in raw throughput
44X reduction in energy consumption
for bulk bitwise AND/OR operations

## Slide 62: Bulk Bitwise AND/OR in DRAM
Copy data of row A to row t1
Copy data of row B to row t2
Initialize data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy data of row t1/t2/t3 to Result row
Copy data of row A to row t1
Copy data of row B to row t2
Initialize data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy data of row t1/t2/t3 to Result row
Result = row A AND/OR row B
Statically reserve three designated rows t1, t2, and t3
MICRO 2013
Notes: * each copy operation takes only 80ns

## Slide 63: Bulk Bitwise AND/OR in DRAM
Copy RowClone data of row A to row t1
Copy RowClone data of row B to row t2
Initialize RowClone data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy RowClone data of row t1/t2/t3 to Result row
Result = row A AND/OR row B
Use RowClone to perform copy and initialization operations completely in DRAM!
Statically reserve three designated rows t1, t2, and t3
Copy data of row A to row t1
Copy data of row B to row t2
Initialize data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy data of row t1/t2/t3 to Result row
Notes: Replace copies with rowclone once it is mentioned
Tie back to the concerns.
Reiterate speedup numbers
strike copy and make it rowclone

## Slide 64: Negation Using the Sense Amplifier
Sense Amp
bitline
bitline
enable
Can we copy the negated value from bitline to a DRAM cell?
Notes: Mark the enable signal to the sense amplifier
Before introducing the dual contact cell, state the key idea

## Slide 65: Negation Using the Sense Amplifier
Sense Amp
Dual Contact Cell
Regular wordline
Negation wordline
bitline
bitline
enable
Notes: Mark the enable signal to the sense amplifier
Before introducing the dual contact cell, state the key idea

## Slide 66: Negation Using the Sense Amplifier
enable sense amp
Sense Amp
½ VDD + δ
½ VDD
VDD
½ VDD
0
activate source
activate
negation wordline
bitline
bitline
source
Notes: Provide the result for NOT
Present all the results after this slide?

## Slide 67: Ambit vs. DDR3: Performance and Energy
Chart: 
| not | and/or | nand/nor | xor/xnor | mean
Performance Improvement | 51.6251 | 38.3193 | 30.6965 | 21.8566 | 32
Energy Reduction | 59.5 | 43.9 | 35.1 | 25.1 | 35
32X
35X

## Slide 68: Integrating Ambit with the System
PCIe device
  Similar to other accelerators (e.g., GPU)
System memory bus
  Ambit uses the same DRAM command/address interface
Pros and cons discussed in paper
(Section 5.4)
Notes: Make it simpler
Two approaches.

## Slide 69: Real-world Applications
Methodology (Gem5 simulator)
  Processor: x86, 4 GHz, out-of-order, 64-entry instruction queue
  L1 cache: 32 KB D-cache and 32 KB I-cache, LRU policy
  L2 cache: 2 MB, LRU policy
  Memory controller: FR-FCFS, 8 KB row size
  Main memory: DDR4-2400, 1 channel, 1 rank, 8 bank
Workloads
  Database bitmap indices
  BitWeaving –column scans using bulk bitwise operations
  Set operations – comparing bitvectors with red-black trees
Notes: Add color
Fix workloads – add set operation workload as well

## Slide 70: Bitmap Indices: Performance
Consistent reduction in execution time. 6X on average
Chart: Execution Time of Query
| w = 2 | w = 3 | w = 4 | w = 2 | w = 3 | w = 4 | n = 8m | n = 16m
Baseline | 27.92 | 41.72 | 54.84 | 58 | 85.44 | 112.92
Ambit | 5.16 | 6.88 | 8.64 | 10.2 | 13.68 | 17.16
5.4X
6.1X
6.3X
5.7X
6.2X
6.6X
Notes: Add color
Remove “week” and “users”

## Slide 71: Speedup offered by Ambit for BitWeaving
Chart: Number of bits for each column value
| 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
1m | 1.8 | 2.7 | 3.5 | 4.1 | 9.6 | 10.6 | 11 | 11.6
2m | 1.8 | 2.8 | 7.6 | 9 | 9.8 | 10.8 | 11.2 | 11.7
4m | 1.8 | 6 | 7.8 | 9.2 | 9.9 | 10.9 | 11.3 | 11.8
8m | 3.9 | 6.1 | 7.9 | 9.2 | 10 | 11 | 11.4 | 11.9
Number of rows in the database table
select count(*) where c1 < field < c2
12X
Notes: Reference bitweaving again
Add color
Fix the tag

## Slide 72
ROW HAMMER
FLIPPING BITS IN MEMORY WITHOUT ACCESSING THEM ISCA 2014

## Slide 73: DRAM CHIP
WORDLINE
ROW
LOW VOLTAGE
HIGH VOLTAGE
VICTIM
VICTIM
AGGRESSOR
READ DATA FROM HERE, GET ERRORS OVER THERE

## Slide 74
GOOGLE’S EXPLOIT
http://googleprojectzero.blogspot.com
“We learned about rowhammer from Yoongu Kim et al.”

## Slide 75
GOOGLE’S EXPLOIT
PROPOSED SOLUTIONS
OUR PROOF-OF-CONCEPT
EMPIRICAL ANALYSIS

## Slide 76: REAL SYSTEM
x86
DRAM
1. CACHE HITS
2. ROW HITS
MANY READS TO SAME ADDRESS
OPEN/CLOSE SAME ROW
≠

## Slide 77
LOOP:
mov (X), %reg
mov (Y), %reg
clflush (X)
clflush (Y)
jmp LOOP
11111111111
11111111111
11111111111
11111111111
Y
X
11111111111
1111
1111
11011110010
10111010111
x86 CPU
DRAM
http://www.github.com/CMU-SAFARI/rowhammer
MANY ERRORS!

## Slide 78
WHY DO THE ERRORS OCCUR?

## Slide 79
DRAM CELLS ARE LEAKY
CHARGE
‘1’
‘0’
64ms
0ms
REFRESH
NORMAL CELL
TIME

## Slide 80
DRAM CELLS ARE LEAKY
CHARGE
‘1’
‘0’
64ms
0ms
REFRESH
VICTIM CELL
AGGRESSOR
TIME

## Slide 81: ROOT CAUSE?
COUPLING
Electromagnetic
Tunneling
⇝
⇝
⇝
⇝
⇝
⇝
⇝
⇝
ACCELERATES CHARGE LOSS

## Slide 82: AS DRAM SCALES …
CELLS BECOME SMALLER Less tolerance to coupling effects
CELLS BECOME PLACED CLOSER Stronger coupling effects
COUPLING ERRORS MORE LIKELY

## Slide 83
ERRORS ARE RECENT Not found in pre-2010 chips
ERRORS ARE WIDESPREAD >80% of chips have errors Up to one error per ~1K cells

## Slide 84
Test Engine
DRAM Ctrl
PCIe
FPGA
PC
DRAM

## Slide 85
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 86: MOST MODULES AT RISK
A VENDOR
B VENDOR
C VENDOR
86%
83%
88%
(37/43)
(45/54)
(28/32)

## Slide 87
MANUFACTURE DATE
ERRORS PER 109 CELLS
MODULES:  A  B  C

## Slide 88: DISTURBING FACTS
AFFECTS ALL VENDORS Not an isolated incident Deeper issue in DRAM scaling
UNADDRESSED FOR YEARS Could impact systems in the field

## Slide 89
HOW TO PREVENT COUPLING ERRORS?
Previous Approaches
1. Make Better Chips: Expensive
2. Rigorous Testing: Takes Too Long

## Slide 90
ROW
MORE ERRORS
ROW
MORE ERRORS
FASTER ACCESS
ROW
ROW
FEWER ERRORS
ROW
FEWER ERRORS
FREQUENT REFRESH
ROW

## Slide 91
Faster ⟶ Slower
ONE MODULE:  A  B  C
ACCESS INTERVAL (ns)
TOTAL ERRORS
55ns
500ns

## Slide 92
Often ⟵ Seldom
ONE MODULE:  A  B  C
REFRESH INTERVAL (ms)
TOTAL ERRORS
64ms
11ms

## Slide 93: TWO NAIVE SOLUTIONS
LIMIT ACCESSES TO ROW Access Interval > 500ns
REFRESH ALL ROWS OFTEN Refresh Interval < 11ms
LARGE OVERHEAD: PERF, ENERGY, COMPLEXITY

## Slide 94: OUR SOLUTION: PARR
Probabilistic Adjacent Row Refresh
Do nothing
Refresh (=Open) adjacent rows
After closing any row ...
0.1%
99.9%

## Slide 95: PARR: CHANCE OF ERROR
NO REFRESHES IN N TRIALS Probability: 0.999N
N=128K FOR ERROR (64ms) Probability: 0.999128K = 10–56
STRONG RELIABILITY GUARANTEE

## Slide 96
STRONG RELIABILITY
LOW PERF OVERHEAD
9.4×10–14 Errors/Year
0.20% Slowdown
NO STORAGE OVERHEAD
0 Bytes

## Slide 97: RELATED WORK
Security Exploit (Seaborn@Google 2015)
Industry Analysis (Kang@SK Hynix 2014) “... will be [more] severe as technology shrinks down.”
Targeted Row Refresh (JEDEC 2014)
DRAM Testing (e.g., Van de Goor+ 1999)
Disturbance in Flash & Hard Disk

## Slide 98: Emerging Memory Technologies

## Slide 99: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 100: Charge vs. Resistive Memories
Charge Memory (e.g., DRAM, Flash)
  Write data by capturing charge Q
  Read data by detecting voltage V
Resistive Memory (e.g., PCM, STT-MRAM, memristors)
  Write data by pulsing current dQ/dt
  Read data by detecting resistance R

## Slide 101: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 102: What is Phase Change Memory?
Phase change material (chalcogenide glass) exists in two states:
  Amorphous: Low optical reflexivity and high electrical resistivity
  Crystalline: High optical reflexivity and low electrical resistivity
PCM is resistive memory: High resistance (0), Low resistance (1)
PCM cell can be switched between states reliably and quickly

## Slide 103: How Does PCM Work?
Write: change phase via current injection
  SET: sustained current to heat cell above Tcryst
  RESET: cell heated above Tmelt and quenched
Read: detect phase via material resistance
  amorphous/crystalline
Large
Current
SET (cryst)
Low resistance
103-104 W
Small
Current
RESET (amorph)
High resistance
Access
Device
Memory
Element
106-107 W
Photo Courtesy: Bipin Rajendran, IBM
Slide Courtesy: Moinuddin Qureshi, IBM

## Slide 104: Opportunity: PCM Advantages
Scales better than DRAM, Flash
  Requires current pulses, which scale linearly with feature size
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
Can be denser than DRAM
  Can store multiple bits per cell due to large resistance range
  Prototypes with 2 bits/cell in ISSCC’08, 4 bits/cell by 2012
Non-volatile
  Retain data for >10 years at 85C
No refresh needed, low idle power

## Slide 105: PCM Resistance → Value
Cell resistance
1
0
Cell value:

## Slide 106: Multi-Level Cell PCM
Multi-level cell: more than 1 bit per cell
  Further increases density by 2 to 4x [Lee+,ISCA'09]
But MLC-PCM also has drawbacks
  Higher latency and energy than single-level cell PCM

## Slide 107: MLC-PCM Resistance → Value
Cell resistance
1
1
0
0
0
1
1
0
Cell value:
Bit 1
Bit 0

## Slide 108: MLC-PCM Resistance → Value
Cell resistance
1
1
0
0
0
1
1
0
Cell value:
Less margin between values
→ need more precise sensing/modification of cell contents
→ higher latency/energy (~2x for reads and 4x for writes)

## Slide 109: Phase Change Memory Properties
Surveyed prototypes from 2003-2008 (ITRS, IEDM, VLSI, ISSCC)
Derived PCM parameters for F=90nm
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
Lee et al., “Phase Change Technology and the Future of Main Memory,” IEEE Micro Top Picks 2010.

## Slide 110: Phase Change Memory Properties: Latency
Latency comparable to, but slower than DRAM
Read Latency
  50ns: 4x DRAM, 10-3x NAND Flash
Write Latency
  150ns: 12x DRAM
Write Bandwidth
  5-10 MB/s: 0.1x DRAM, 1x NAND Flash
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 111: Phase Change Memory Properties
Dynamic Energy
  40 uA Rd, 150 uA Wr
  2-43x DRAM, 1x NAND Flash
Endurance
  Writes induce phase change at 650C
  Contacts degrade from thermal expansion/contraction
  108 writes per cell
  10-8x DRAM, 103x NAND Flash
Cell Size
  9-12F2 using BJT, single-level cells
  1.5x DRAM, 2-3x NAND (will scale with feature size, MLC)

## Slide 112: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatile  Persistent
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
  Reliability issues (resistance drift)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system

## Slide 113: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM

## Slide 114: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 115: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 116: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 117: Architecting PCM to Mitigate Shortcomings
Idea 1: Use multiple narrow row buffers in each PCM chip
     Reduces array reads/writes  better endurance, latency, energy
Idea 2: Write into array at
cache block or word
granularity
 Reduces unnecessary wear
DRAM
PCM

## Slide 118: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 119: PCM As Main Memory
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf)

## Slide 120: Review #5
Flipping Bits in Memory Without Accessing Them Yoongu Kim et al., ISCA 2014

## Slide 121: CSC 2224: Parallel Computer Architecture and Programming Advanced Memory
Prof. Gennady Pekhimenko
University of Toronto
Fall 2020
The content of this lecture is adapted from the slides of
Vivek Seshadri, Yoongu Kim,
and lectures of Onur Mutlu @ ETH and CMU